Intro
EDA – March 2007 @ ULP
EDA
Electronic Design Automation

---
Agenda
ChitleshGoorah
Post Graduate Student In
Micro Nano Electronic Engineering
Open Source Tools for Electrical and Electronic Engineers
(Desktop Applications used by circuit designers)
How professional work can be done with Open Source Software

---
Simulations

---
Analog Simulations
Analog Simulations
Schematic Capture
Kicad and gEDA/gaf Suites
PCB, PCBboard, allegro, eagle, futurenet2, protelII, redac,
 spice, Switcap, systemc, vams, verilog, vhdl, vipec
Netlist
Spice, spice-sdb, VHDL, Verilog, PCB
Simulation
GHDL, FREEHDL (qucs)
Icarus Verilog
NgSpice: (Simulation Program for Integrated Circuit Emphasis)
netlist format
Simulator
Layout

---
SPICE
gnetlist -g spice-sdb my_schematic.sch
*********************************************************
* Spice file generated by gnetlist *
* spice-sdb version 12.27.2005 by SDB -- *
* provides advanced spice netlisting capability. *
* Documentation at http://www.brorson.com/gEDA/SPICE/ *
*********************************************************
*vvvvvvvv Included SPICE model from /usr/share/gEDA/models/ua741.inc vvvvvvvv
* UA741 operational amplifier "macromodel" subcircuit
* created using Parts release 4.01 on 07/05/89 at 09:09
* (REV N/A)
* connections: non-inverting input
* | inverting input
* | | positive power supply
* | | | negative power supply
* | | | | output
* | | | | |
.subckt UA741 1 2 3 4 5
[...]
.model dx D(Is=800.0E-18)
.model qx NPN(Is=800.0E-18 Bf=62.50)
.ends
*^^^^^^^^ End of included SPICE model from /usr/share/gEDA/models/ua741.inc ^^^^^^^^
*
*============== Begin SPICE netlist of main design ============
R2 2 1 100K
R1 3 2 10K
[...]
Vee 4 0 DC -12V
.end
Spice models from vendors
subckt
Schematic Capture to Netlist

---
PCb
PCB,
printed circuit board layout editor.
Like gEDA/gaf,
symbols can easily be made

---
Analog_Demo
gEDA (gschem)
KICAD

---
Layout
Simulation of the Layout
Magic
a VLSI layout editor, extraction, and online DRC tool.
With open source VLSI engineers with a bent toward programming to implement clever ideas
simulations with IRSIM

---
Checks
Design Rule Check
Layout Vs. Schematic check
Checking non-numbered parts...
Checking duplicated references...
Checking nets with only one connection...
Checking pins without the 'pintype' attribute...
Checking type of pins connected to a net...
Checking unconnected pins...
Checking slots...
Checking duplicated slots...
Checking unused slots...
No warnings found.
No errors found.
Layout - Netlist comparison (LVS)
With Netgen

---
Logic Simulations
Logic Simulation
Xcircuit
circuit drawing and schematic capture tool.
(one click conversion to sim netlist)
| sim circuit "buffer" from XCircuit v3.40 rev 26
n In1 GND signal
n signal GND Out
p In1 Vdd signal
p signal Vdd Out
IRSIM
event driven logic simulator for MOS

---
Hard_Work
opencircuitdesign.com
geda.seul.org
Widespread use for both
board and chip design

---
Q&A
Questions & Answers